Application Specific Instruction set Processor Design
Application Specific Instruction set Processor Design
Nikolaos Kavvadias
April 2003
(converted to .odp: 2010/11/25)
Electronics and Computers Div.,
Department of Physics,
Aristotle University of Thessaloniki,
54124, Thessaloniki, Greece
E-mail: nkavv@physics.auth.gr

---
PowerPoint Presentation
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for synthesis of Application Specific Instruction Sets
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Outline
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for joint design of instruction sets and micro-architectures
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Main challenges in embedded systems design
Embedded systems form a market that is growing more rapidly than that of general purpose computers
Embedded processors are extensively used in digital wireless communications and multimedia consumer electronics (e.g. cellular phones, video cameras, audio players, video-game consoles)
These complex systems relay on power hungry algorithms
The portability of these systems makes energy consumption a particularly critical design concern with performance and cost
At the same time, levels of microelectronic integration continue to rise enabling more integrated functionality on a single chip

---
Main challenges in embedded systems design (2)
Basic challenge:
How to effectively design first-time-right complex systems-on-a-chip that meet multiple stringent design constraints?
To do that it is important to maximize the flexibility/programmability of the target system architecture moving as much functionality as possible to embedded software
General purpose embedded processors may not be able to deliver the performance required by the application and they may be prohibitively expensive/inefficient, e.g. to energy consumption
Thus, the embedded systems industry has shown an increasing interest in Application-Specific-Set Processors (ASIPs)

---
What are ASIPs
Processors designed for a particular application or set of applications
An ASIP is designed to exploit special characteristics in the target application in order to meet performance, cost and energy requirements
By spending silicon where it truly matters, these processors are smaller and simpler than their general-purpose counterparts, able to run at higher clock frequencies and more energy efficient
Obtaining best results requires proper decisions at the joint instruction set and micro-architectural level
Considered as a balance between two extremes: ASICs and general-purpose processors

---
Potential benefits from adopting an ASIP solution
Benefits of an ASIP solution:
Maintain a level of flexibility/programmability through an instruction set
Overcome the problems of conventional RISC/DSP architectures:
a. Fixed level of parallelism which may prove inefficient for real-time applications of high computational complexity
b. Prohibitively high energy consumption
c. Time-critical tasks that require the incorporation of dedicated hardware modules
Shortening of debugging/verification time. Key enabler is FPGA technology (rapid prototyping/reconfigurable platforms)

---
Challenges in ASIP design
Given an application or set of applications, the design of an instruction set and micro-architecture to meet the design constraints of area, performance and energy consumption requires:
Definition of the design space of both instruction sets and micro-architectures to be explored
Understanding of the relationships between application characteristics and design (mapping of application on hardware)
Development of tools (assembler/linker, compiler backend and frontend, simulator, debugger) for efficient design space exploration

---
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for synthesis of Application Specific Instruction Sets
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Issues in application-specific processor design
Instruction Set Synthesis (ISS)
Generates an instruction set that optimizes an objective function (instruction set size, cycle count, cycle time, gate count)
Instruction Set Mapping (ISM) or Code Generation (CG)
Systematic mapping of the application into assembly code with the given instruction set
Microarchitecture Synthesis (MS)
Given an instruction set specification, this approach synthesizes a micro-architecture at the RTL, which implements the instruction set

---
Steps in ASIP Synthesis
Steps in ASIP Synthesis
Main steps in a typical methodology for ASIP synthesis:
Application analysis
Architectural design space exploration
Instruction set generation
Code synthesis
Hardware synthesis

---
Flow Diagram of a typical ASIP Design Methodology
Flow Diagram of a typical ASIP Design Methodology
Application &
Design Constraints
Application Analysis
Architectural Design Space Exploration
Instruction Set
Generation
Code Synthesis
Hardware Synthesis
Object Code
Processor Description

---
Application analysis
Application analysis
Input in the ASIP design process is an application or a set of applications
The target application(s) along with its test data and design constraints are analyzed either statically (profilers) or dynamically
Major task is to extract coarse-level requirements (micro-operations) which will lead the instruction set and micro-architecture design procedure
Dynamic profiling: The original application description, in a high-level language is instrumented with performance counters and the modified application code is executed

---
Application analysis (2)
Application analysis output may includes:
number of operations and functions
frequency of individual instructions and sequence of contiguous instructions
average basic block sizes
data types and their access methods
ratio of address computation instructions to data computation instructions
ratio of input/output instructions to total instructions
It serves as a guide for the subsequent steps in ASIP synthesis

---
Architectural Exploration
It is important to deside about a processor architecture suitable for target application
Determination of a set of architecture candidates for a specific application(s) given the design constraints
Performance, hardware cost and power consumption estimation and selection of the optimum one
Performance estimation can be based on scheduling or simulation

---
Architectural Exploration (2)
Block diagram for a typical architecture explorer
The selection process typically can be viewed to consist of a search technique over the design space driven by a performance estimator

---
Architecture design space
Need for a good parameterized model of the architecture
Different values should can be assigned to the parameters while keeping design constraints into consideration
The size of the design space is defined by the number of parameters and the range of values which can be assigned to these paramters

---
Architecture design space (2)
Parameters of architecture models:
- number of functional units of different types
- storage elements
- interconnect resources
- pipelining
- number of pipeline stages
- instruction level parallelism
- addressing support
- memory hierarchy
- instruction packing
- latency of functional units and operations
All parameters together support a large design space

---
Scheduling-based performance estimation
Scheduling-based performance estimation
Architecture
Description
Application
Profiler
Retargetable
Estimator
Performance and
other Estimates
The problem is formulated as resource constrained scheduling problem with the selected architectural components as the resources and the application is scheduled to generate an estimate of the cycle count

---
Simulation-based performance estimation
Simulation-based performance estimation
Retargetable
Compiler
Simulator
Application
(HLL)
Object
Code
Architecture
Description
Trace Data
The application is mapped on a simulation model of the architecture for performance estimation

---
Simulation-based performance estimation (2)
A simulation model of the architecture is generated and the application is simulated to compute the performance
The application is translated into an intermediate code composed of simple instructions directly expressing primitive hardware functionalities
A sequential code simulation is performed to validate the code and to extract early features which can perform preliminary architectural choices
The simulator reports performance energy consumption and statistics about resource utilization
Optimization techniques are applied to increase the degree of parallelism
Frequently executed sequence of instructions can be subistuted by the introduction of new instructions

---
Instruction set generation (synthesis)
Instruction set generation (synthesis)
Instruction set is synthesized for a particular application based on the application requirements, quantified in terms of the required micro-operations and their frequencies
A methodology for instruction set synthesis should utilize:
A model for the micro-architecture
An objective function that establishes a metric for the fitness of the solution (both instruction set and micro-architecture)
Design (hardware resource and timing) constraints are considered
In the approach to be discussed [Huang95] instruction set design is shown as a modified scheduling problem of the application micro-operations. At the same step, instruction set and application code is generated

---
Code Synthesis: Retargetable code generator
Instruction set
Architecture (ISA)
Application
(HLL)
Architecture
template
Retargetable code generator
Object code
Retargetable code generator: The architecture template and instruction set architecture and application are accepted as inputs, in order to generate object code

---
Code Synthesis: Compiler generator
Code Synthesis: Compiler generator
Instruction set
Architecture (ISA)
Application
(HLL)
Architecture
template
Retargetable compiler generator
Customized compiler
Object code
Compiler generator (or Compiler – Compiler): Accept architecture template and instruction set as inputs and generate a customized compiler which accepts the application programs

---
Hardware synthesis
Hardware synthesis refers to the generation of the HDL descriptions for the processor modules
Automatic generation of RTL descriptions, for both simulation (and functional verification) and logic synthesis purposes
Instruction set
Architecture (ISA)
Design
constraints
Architecture
template
Automatic hardware generation
VHDL description
of the processor

---
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for synthesis of Application Specific Instruction Sets
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Key issue in designing efficient ASIPs
The performance of a microprocessor-based system depends on how efficiently the application is mapped to the hardware
Key issue determining the success of the mapping is the design of the instruction set
A jointly design of the instruction set and microarchitecture is required
Here the following ASIP design methodology is presented:
I.J. Huang and A.M. Despain, “Synthesis of Application Specific Instruction Sets,” IEEE Transacions on Computer Aided Design, vol 14, June 1995

---
Presented ASIP design methodology
The design problem is formulated as a modified scheduling problem
The application is represented by micro-operations
The micro-operations are scheduled on a parameterized pipelined micro-architecture folowing the design constraints
Instructions are formed by an instruction formation process which is integrated into the scheduling process
The compiled code of the application is generated using the synthesized instruction set
A simulation annealing scheme is used to solve for the schedule and the instruction set

---
Models for instruction sets
Models for instruction sets
An instruction contains one or more parallel micro-operations (MOPs)
MOPs are controlled via instruction fields belonging to some field types
The instruction word length is defined by the designer (e.g. 32 bits)
Example of instruction field types and corresponding bit-widths

---
Instruction formats
Instruction formats
Examples of instruction formats
Example 1: The ADD instruction
Instruction description: add(R1,R2,immed)
Corresponding MOP: R1 <- R2 + immed
Example 2: INC instruction
Instruction description: inc(R)
Corresponding MOP: R <- R + 1 (21 bits unused in the format)

---
Operand encoding
Operand encoding
The operands of instructions can be encoded to become part of the opcode in two ways:
A specific value can be permanently assigned to an operand and becomes implicit to the opcode (eg. Immed=1)
Unifying the register specifiers (eg. R1=R2)
Encoding operands saves instruction field, at the cost of possibly larger instruction set size, additional connections and hardwired constants in the datapath

---
Operand encoding (2)
Operand encoding (2)
Encoding allows more MOPs to be packed into a single instruction
Example: if it happens very often that the values of two independent
registers are increased by one at the same time, a new instruction can be considered
Incd(R1,R2) => ‘R1<-R1+1; R2<-R2+1’ using only 16 bits
while the generalized form ‘R1<-R2+Immed1; R3<-R4+Immed2’
uses 58 bits violating the design constraints (32 bits)

---
Basic pipeline micro-architecture model
Basic pipeline micro-architecture model
Processor operation can be functionally partitioned into 6 pipeline stages
Variations to the basic pipeline structure:
1. IF-ID/R-A-M-W: 5-stage MIPS-like pipeline, single format for registers
2. IF-ID-R-A/M-W: 5-stage pipeline, no displacement addressing

---
Pipeline micro-architecture details
Pipeline micro-architecture details
The pipeline is controlled in a data-stationary fashion
Data-stationary control: the opcode flows through the pipeline in synchronization with the data being processed in the data path
Pipeline stage controllers: At each stage, the opcode together with the possible status bits from the data path, is decoded to generate the control signals necessary to drive the data path.

---
Pipeline micro-architecture details (2)
Pipeline micro-architecture details (2)
This RISC-style pipeline supports single-cycle instructions
Multiple-cycle instructions can be accommodated if execution can be stalled to wait for multi-cycle functional units to complete
More generally, multiple-cycle arithmetic/logic operations, memory access, and change of control flow (branch/jump/call) are supported by specifying the delay cycles as design parameters

---
The specification for the target micro-architecture
The specification for the target micro-architecture
The target micro-architecture can be fully described by specifying the supported MOPs and a set of parameters
The supported MOPs describe the functionality supported by the micro-architecture, and the connectivity among modules in the data path

---
The specification for the target micro-architecture (2)
Example of micro-operations
The pipeline configuration IF-ID/R-A-M-W is used
The pipeline configuration IF-ID-R-A/M-W can be used by eliminating rmd, mrd and mrad

---
Micro-architecture parameters
Micro-architecture parameters
The set of parameters describes resource allocation and timing
Examples of parameters:
number of register file read/write ports (R/W)
number of memory ports (M)
number of functional units (F)
size of register file and memory
latencies of operations (multi-cycle functional units)
delay cycles between operations (registering/bypassing outputs)

---
Micro-architecture parameters (2)
Micro-architecture parameters (2)
Example of resource size and latency parameters
Example of delay cycle parameters (can model bypassing buses)

---
Instruction format and hardware costs
Instruction format and hardware costs
Each MOP supported by the data path is assigned costs for the instruction format and hardware resources
Instruction format costs:
instruction fields, including register index, function selectors and immediate data
Hardware costs:
hardware resources as read/write ports of the register file, memory ports, and function units

---
Models for application benchmarks
Models for application benchmarks
Each application benchmark is represented as a group of basic blocks
Basic block: sequential code between consecutive control flow boundaries
Basic block weights are determined dynamically by profiling, and is usually used to indicate how many times the basic block is executed in the benchmark
An initial specification for the required MOPs is defined
The basic blocks are mapped to control/data flow graphs (CDFGs) of MOPs based on the given MOP specification
Different micro-architectures result in different MOP specifications, which may map the basic blocks to different CDFGs

---
Basic block representation
Basic block representation
Example: CDFG for the MOPs of simple basic block
Control dependencies are represented by dashed arrows
Data-related dependencies are represented by solid arrows

---
Synthesis of Instruction set
The instruction set design problem can be formulated as a modified scheduling problem
Application
(CDFGs)
Design constraints
Objective function
μ-Arch. Specs
Scheduling
Instruction
Formation
Instruction set
Compiled code
The MOPs in the CDFG are scheduled into time steps, subject to various constraints
While scheduling MOPs into time steps, instructions are formed at the same time

---
Examples of micro-operation schedules
Examples of micro-operation schedules
Example schedule 1 for the simple basic block:
This is a serialized schedule with 1 MOP per time step
One-cycle delay for the jump MOP and zero cycle delay for the MOPs are assumed

---
Examples of micro-operation schedules (2)
Examples of micro-operation schedules (2)
Example schedule 2 for the simple basic block:
A more compact schedule with four cycles
The delay slot of MOP6 is filled with MOP5 such that there is no need for a nop MOP

---
Instruction formation details
Instruction formation details
The semantics of an instruction can be represented by a binary tuple <MOPTypeIDs, IMPFields>, where MOPTypeIDs is a list of type IDs of MOPs contained in the instruction and IMPFields is a list of fields that are encoded into the opcode
Example 1: add(R1, R2, immed) is represented by <[rrai], []>
The MOP type ID contains MOP: R1 <- R2 + immed
No fields are encoded (second argument of the tuple is empty)
Example 2: inc(R) is represented by <[rrai],[R1=R2, immed=1]>
inc instruction is an encoded version of the add (same MOPType ID)
R1=R2 unifies the corresponding register specifiers, and immed=1 assigns the immediate operand a fixed value
Instructions are generated from time steps in the schedule, with each time step corresponding to one instruction

---
Code generation resulting from the scheduling/instruction formation process
Code generation resulting from the scheduling/instruction formation process
The compiled code can be obtained easily from the instruction names and instantiated field values
Example: Compiled code from the scheduled basic block of second Table
inst7(r2, r0, 0)
inst7(r2, r1, 1)
inst5(1024)
inst4(r2, r2, 2)
The instruction set is formed by taking the union of instructions generated from all time steps eg. inst4, instr5, instr7

---
Performance (cycle count) and Costs
Performance (cycle count) and Costs
Execution cycles is determined as the weighted sum of the lengths (number of time steps) of the scheduled basic blocks in the benchmark
The length of the basic cost includes nop slots which are inserted by the design process to preserve the constraints due to multi-cycle operations
The design process will try to eliminate the nop slots by reordering other independent operations into the nop slots
Each instruction has two costs associated with it
The total number of bits required to represent the instruction
Hardware costs (the collection of the resources required by all MOPs contained in the instruction, minus the shared resources
The global hardware resources are obtained by choosing the maximal number for each resource type from all instructions

---
Increase the efficiency of the instruction set
Compact and powerful instructions can be synthesized by:
packing more MOPs into a single instruction
making fields implicit
making register ports unified to satisfy the cost constraints
This is particularly useful in an application specific environment where instruction sets can be customized to produce compact and efficient codes for the intended applications

---
Types of constraints
Types of constraints
The MOPs are scheduled into times steps while data/control dependencies and timing constraints (for multi-cycle MOPs) have to be satisfied
Data dependent MOPs have to be scheduled into different time steps, subject to the precedent relationship and timing constraints (except single cycle MOPs with Write-after-Read dependencies)
In case of control dependency with a timing constraint, e.g. a delayed jump
The MOPs that are data-independent to the jump/branch MOPs can be scheduled into the time step before the jump/branch MOPs or the delay slots after the jump/branch MOPs
The length of the delay slots is determined by the timing constraint
Other constraints: instruction word width, hardware resources consumed by the instructions, the size of the instruction set that the opcode field can afford

---
Objective function
Objective function
An objective function is necessary to control the performance/cost trade-off
The goal of the design system is to minimize a given object function
The objective function has to account for parameters as:
cycle count C (as determined by the performance metrics)
instruction set size S (represents the cost metrics)
improvement in performance compared to other candidates, P
Objective = (100/P) • ln(C) + S
The design constraints are either captured by the objective function (not in this case) or examined separately

---
Simulated annealing algorithm
Simulated annealing algorithm
The instruction set design problem is formulated as a scheduling problem
The scheduling problem is solved by a simulation annealing scheme
An initial design state consisting of an initial schedule and its derived instruction set (generated by a preprocessor) is given to the design system
then a simulated annealing process is invoked to modify the design state in order to optimize the objective function
The simulated annealing process is run until the design state achieves an equilibrium state

---
The basic simulated annealing algorithm
The basic simulated annealing algorithm
At each temperature (outer while loop), several movements (changes of the design state) are generated by the inner while loop. The number of movements is specified by the designer

---
Move operators
Move operators
Move operators are applied to change the design state
They provide methods of manipulating the MOPs and time steps
Move operators can be classified into three groups
Manipulation of the instruction semantics and Format of a selected time step
Manipulation of MOPs locations
Micro-architecture-dependent operators (include methods that explore the special properties of the target micro-architectures)

---
Manipulation of the instruction semantics and format
Manipulation of the instruction semantics and format
Unification: Unify two register accesses in the MOPs (e.g. R1=R2 in inc(R)). Decreases the instruction word width and register read/write ports
Split: Cancel the effect of the unification operator. Increases the instruction word width and register read/write ports
Implicit value: Bind a register specifier to a specific register, or an immediate data field to a specific value (as immed=1 in the inc). Decreases the instruction word width
Explicit value: Cancel the effect of the “implicit value” operator. Increase in the instruction word width
Generalization: Encoded operands in an instruction format are made general (explicit in the instruction fields). Increased instruction word width and hardware resources

---
Manipulation of MOP’s locations
Manipulation of MOP’s locations
These move operators are subject to the data/control dependencies and delay constraints when moving MOPs
Interchange: Interchange the locations of two MOPs from different time steps. Changes the semantics and formats of the two instructions in the corresponding time steps
Displacement: Displaces a MOP to another time step. Simplifies the instruction in the original time step and enriches the instruction in the destination time step
Insertion: Insert an empty time step after or before the selected time step and move one MOP to the new time slot. Increases the cycle count
Deletion: Delete the selected time step if it is an empty one. Decreases the cycle count
The move operators may change the resource usage in the selected time steps.

---
Micro-architecture dependent operators
Micro-architecture dependent operators
These move operators explore the special properties of the target micro-architectures
Example: Tradeoffs in functional unit interconnections
- The target micro-architecture provides two data routing possibilities:
1. register file  functional unit  register file
2. register file  register file
- Then, the following MOPs are equivalent:
1. rrai: R1  R2 + Immed (Immed=0)
2. rr:	R1  R2
- These have different costs in hardware and instruction format and can be transformed from one to another

---
Example: Changing the design state with move operators
Example: Changing the design state with move operators
In the following tables, a sequence of operators are applied to transform the schedule (one design state) to a better design state
1) Displacement: displace the MO2 from time step 2 to 1

---
Example: Changing the design state with move operators (2)
Example: Changing the design state with move operators (2)
2) Unification: unify fields D1 and D2 in time step 1
3) Unification: unify fields D1 and I in time step 1
4) Unification: unify fields R1 and R2 in time step 1
5) Unification: unify fields R1 and R4 in time step 1

---
Example: Changing the design state with move operators (3)
Example: Changing the design state with move operators (3)
6) Deletion: delete the empty time step 2
7) Displacement: displace the MO4 from time step 4 to 3

---
Example: Changing the design state with move operators (4)
Example: Changing the design state with move operators (4)
8) Deletion: delete the empty time step 4
9) Unification: unify fields D1 and I in time step 3
10) Unification: unify fields R1 and R4 in the time step 3
11) Displacement: displace the MO5 from time step 5 to 7 (see table above)
12) Deletion: delete the empty time step 5

---
Heuristics for target selection
Heuristics for target selection
During each iteration, the design space is examined whether it violates the design constraints
In case of constraint violation a time step is randomly selected from a pool of time steps that violate design constraints
If more than one constraint are violated, the hardware resource violations get higher priority than instruction word width violations
Instruction word width violations: one of the following move operators is applied randomly: “unification”, “implicit value”, “interchange”, “displacement”, “insertion”
Resource violations: one of the following move operators is applied randomly: “unification” (register port constraint), “implicit value”, “displacement”, or “insertion”

---
Selection weights
Selection weights
In case of no constraints, all move operations are eligible for changing the design state
A basic block is selected with the probability Selectioni which is the selection weight of the basic block i
Fi: execution frequency of the basic block
Ni: number of MOPs in the basic block
The selection weight is intended to denote the degree of importance of a basic block in the benchmark

---
Temperature and Cooling schedule
Temperature and Cooling schedule
The cooling schedule is controlled by five parameters
1) Initial temperature (T0). It should be high enough so that there is no rejection for high-cost states at the initial temperature
2) The number of movements (M) tried at each temperature. These are proportional to the total number of MOPs in the benchmarks.
3) The next temperature (T) of the current temperature (e.g. 90%)
4) Low and high temperature points. A low temperature point is defined such that a special handling routine can be applied to stabilize the design. Different move acceptance rules are applied	to high temperature points
5) The number of consecutive temperature points that the design state has remained unchanged. At such point, the annealing process is terminated

---
Move acceptance
Move acceptance
Conditions for movement acceptance:
1) The movement reduces the value of the objective function
2) The movement is a result of constraint resolution
3) Otherwise: a movement is accepted with a exp-(Δ/T) probability where Δ is the increased value of the objective function, T the current temperature

---
Design Flow of the presented methodology
Design Flow of the presented methodology
Steps in the instruction set design process
1) The given application is translated to dependency graphs of MOPs which are supported by the given architecture template
the application is written in a high-level language and an intermediate representation is generated by a compiler frontend
a retargetable MOP mapper transforms the intermediate representation into the dependency graphs of MOPs

---
Design Flow of the presented methodology (2)
Design Flow of the presented methodology (2)
2) A preprocessor generates a simple schedule for the MOPs
the schedule is obtained by serializing the dependency graphs. An initial instruction set is then derived from the schedule by directly mapping time steps into instructions without encoding any operand
The obtained schedule and instruction set constitute the initial design state
3) The simulated annealing algorithm is invoked to optimize the design state
Several trial runs of the algorithm may be necessary to adjust the cooling schedule
Output of the design flow: the best instruction set, micro-architecture, and assembly code which minimizes the objective function can be obtained after the design state reaches the equilibrium state

---
A small example
A small example
A small benchmark is examined, consisting of 18 MOPs. It is a list-creating application in Prolog
bf: before dependencies between MOPs
ctl: denotes control dependencies

---
A small example (2)
A small example (2)
The 32-bit and 64-bit instruction sets were synthesized, with resource constraints <3R,1W,2M,1F> and <6R,4W,4M,4F>, respectively
synthesized 32-bit instruction set
synthesized 64-bit instruction set

---
A small example (3)
A small example (3)
The 32-bit instruction set compiles the application in 12 clock cycles, whereas the compiled code for the 64-bit instruction set consists of 9 cycles
compiled code for the 32-bit instruction set
compiled code for the 64-bit instruction set

---
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for synthesis of Application Specific Instruction Sets
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Architecture design space exploration
Architecture design space exploration
A method is presented for architecture design space exploration to support instruction set generation from target applications
The target application is selected from the multimedia field (requirement of high performance and low energy consumption for efficient manipulation of large amounts of data in real time)
Architectures with different configurations in terms of hardware resource selection and interconnection are explored in order to study the execution performance and power/energy consumption tradeoffs
For this reason:
A flexible and parametric processor model is defined and analyzed
Pre-characterized hardware units in terms of area, delay and power consumption are required
A cycle-accurate instruction set simulator with energy consumption capability is implemented

---
Proposed architecture model
Proposed architecture model
Architecture template: four-stage pipeline, Harvard bus architecture, data stationary control
Pipeline operation:
instruction fetch (IF)
instruction decode and operand fetch (ID)
execute and memory read (EX)
write-back (WB)
Pipeline stalls occur: for data memory accesses at the EX stage, during operation in multi-cycle functional units, conditional executed instruction is not satisfied
Pipeline flush: alteration of control flow
Early completion path at the end of EX stage (e.g. for control-flow instructions)

---
Block diagram of the proposed architecture model
Block diagram of the proposed architecture model

---
The proposed approach for ASIP design space exploration
The proposed approach for ASIP design space exploration
Application analysis: extract weights for the coarse-level requirements
Application description: the application is documented in basic blocks in the form of MOPs
MOPs are defined only for the frequently executed operations satisfied by corresponding hardware resources
Scheduling of the MOPs: the MOPs are scheduled into time steps, taking into account architecture characteristics, resource allocation and timing constraints
Instruction generation: instructions are generated from time steps in the schedule. Possibility of multi-cycle instructions
Performance estimation: the MOP description for the target application is simulated on the modified architecture model to evaluate the effect of the architecture changes

---
Performance estimation
Performance estimation
A retargetable cycle-accurate simulator is created for design verification and performance/power estimation
Architecture changes are incorporated in the simulator
The simulator is updated with the characteristics of the hardware resources
Performance estimation: the simulator accounts for the cycle count, number of issued and executed instructions.
Energy estimation: average power and total energy consumption are calculated by adding the contributions from each functional and storage resources
Area estimation: count of equivalent gates
The simulator utilizes pre-characterized resource models derived from PEAS-III framework

---
Outline
Challenges in ASIP design
Introduction to the ASIP design flow
A methodology for synthesis of Application Specific Instruction Sets
Architecture design space exploration for ASIPs
Case study: ASIP design for an image compositing application

---
Case study: Image compositing
Case study: Image compositing
Case study: Image compositing application (alpha blending) for the visual part of MPEG-4
A common technique in computer graphics and visualization to perform simple compositing of digital images
This version of the algorithm follows a block-based processing approach, and consists of two double-nested loops. A simple case is assumed with 1 foreground and 1 background objects of the same size

---
Application analysis for the case study
Application analysis for the case study
The alpha blending algorithm is described in C code. Here is the corresponding pseudocode
for i in 0 to H/B, step B
for j in 0 to W/B, step B
for k in 0 to B, step 1
for l in 0 to B, step 1
temp = alpha*img_in1[B*i+k][B*j+l] +(255-alpha)*img_in2[B*i+k][B*j+l];
img_out[B*i+k][B*j+l] = (temp>>8);
endfor;
endfor;
endfor;
endfor;

---
Code instrumentation for the application
Code instrumentation for the application
Performance counters are inserted in the application code in order to perform dynamic profiling
for i in 0 to H/B, step B
for j in 0 to W/B, step B
for k in 0 to B, step 1
for l in 0 to B, step 1
temp = alpha*img_in1[B*i+k][B*j+l] +(255-alpha)*img_in2[B*i+k][B*j+l];
c_Mread+=8; c_Mwrite+=1; c_add+=1; c_mult+=2; c_sub+=1; c_address_add+=4;
c_address_mult+=2;
img_out[B*i+k][B*j+l] = (temp>>8);
c_Mread+=1; c_Mwrite+=1; c_shift+=1;
// c_address_add+=2; c_address_mult+=2;
// addresses B*i+k, B*j+l already available from the previous operation
endfor;
endfor;
endfor;
endfor;

---
Dynamic profiling results and discussion
Dynamic profiling results and discussion
A result file is generated with the extracted information
RESULT FILE for Alpha Blending algorithm
Filename: ablend_c_report.txt
Parameters: H=288, W=352, B=8
-----------------------------------------------------------
Number of adds:101376
Number of multiplies:202752
Number of address stepping operations:115668
Number of address add operations:405504
Number of address multiply operations:202752
Number of memory element reads:912384
Number of memory element writes:202752
Number of subtracts:101376
Number of shifts:101376

---
Micro-operation description for the application
Micro-operation description for the application
The initial MOP description for the application
movi Rix3, 0
movi Rfin3, 7
loop3:
mul R6, R3, Rix0
add R6, R6, Rix2
mul R7, R3, Rix1
add R7, R7, Rix3
mul R8, R6, R2
add R8, R8, R7
movi R13, 0
shl R13, R13, 8
ld R9, R8, R13
movi R13, 99
shl R13, R13, 8
ld R10, R8, R13
rsbi R6, R0, 255
mul R7, R0, R9
mul R11, R6, R10
add R12, R7, R11
… (MOPs for storing temp)
addi Rix3, Rix3, 1
cmp Rix3, Rfin3
blt loop3
for l in 0 to B-1, step 1
temp = alpha*img_in1[B*i+k][B*j+l] +
(255-alpha)*img_in2[B*i+k][B*j+l];
…
endfor;

---
Baseline architecture for the image compositing ASIP
Baseline architecture for the image compositing ASIP
In the first step, we derive a baseline architecture for the ASIP
Architecture parameters:
single ALU
single-cycle array multiplier
shifter with left/right shift capability
single register file with 3 read ports and 1 write port
dedicated adder for PC update
local (on-chip) instruction and data memory
The application is analyzed in MOPs and implemented by appropriate scheduling of these in time steps. MOPs in the same time step identify an instruction with needed resources
The initial instruction set consists of 13 instructions (following table)

---
Baseline architecture for the image compositing ASIP(2)
Baseline architecture for the image compositing ASIP(2)
Initially, instruction and data sizes are restricted to 32 bits. Finally, we select 28-bit fixed length instructions and 24-bit datapath
Since a full-sized array multiplier presents significant propagation delay, we have selected two-stage multiplier implementation
Instructions present a CPI of 1 except: load register from memory (stall in EX stage, so 2 incremental cycles are required), multiply instruction (2 incremental cycles)

---
Extracted instruction set
Extracted instruction set
“Inst. Definition” column shows the instruction counterparts to which the micro-operations are mapped

---
Architectural modifications to the basic instruction set/ micro-architecture
Architectural modifications to the basic instruction set/ micro-architecture
Modifications are applied to the initial specification of the ASIP and three different configurations are produced
Version 1: Effect of register file topology (additional register files are introduced to store the index values for the loops in the algorithm)
Version 2: Effect of implementing the multiply-add operation
Version 3: Effect of replacing chainable operations by single instructions (the packing of MOPs produces alternative instructions
The effect of these modifications on cycle performance and energy consumption is evaluated in our cycle-accurate simulator

---
Version 1: Effect of register file topology (tradeoffs)
The registers in the initial register file are reduced from 32 to 16 and 3 additional register files are used to store the running index, final and step values
The index register files consist of 4 12-bit registers with 2 read and 1 write ports
Tradeoffs in version 1 of the ASIP:
For each register file, a separate address may be required, and this overhead has to be compensated by the reduction in energy consumption due to fewer storage bits
The use of different data widths in the datapath requires the use of size-extension circuitry, which negatively affects propagation delay
Results:
The number of execution cycles is not affected
Energy consumption is reduced by 20%

---
Version 2: Effect of the Multiply-Add operation
Version 2: Effect of the Multiply-Add operation
The resulting architecture (version 1) is used as input to subsequent design space exploration steps
Application analysis has identified a frequent pattern consisting of the MUL and ADD micro-operations
A new instruction, MADD, is designed that incorporates the MUL and ADD micro-operations in the same control step
An adder (in the ALU) and a multiplier were already included in the original configuration, so only minimal changes to the interconnection of these units are required
Results:
Reduction of 12% in the clock cycles and 17% in the energy consumption are observed (against version 1)

---
Version 2: Effect of the Multiply-Add operation (explanation)
Version 2: Effect of the Multiply-Add operation (explanation)
Pattern matching for the MUL-ADD micro-operation couple
MUL R8, R6, R2
ADD R8, R8, R7
MAC R8, R6, R2, R7
Assembly code for version 2 of the ASIP
Baseline assembly code
Micro-operation description for the MAC operation
Instruction format: MAC Rd, Rs1, Rs2, Rs3 (D-format)
Action: Rd  (Rs1*Rs2) + Rs3

---
Version 3: Effect of replacing chainable operations by single instructions
Version 3: Effect of replacing chainable operations by single instructions
The MOVI-SHL couple is replaced by a move immediate and shift left instruction (MVISL)
An instruction for loop increment and conditional branch is inferred from an ADDI-CMP-BLT operation pattern (FOR instruction)
The modifications required are the inclusion of a dedicated adder and multiplexing for calculating loop specifying the running index register, with final and step index registers implicitly encoded
The average power consumption is indices
In the FOR instruction definition, two register fields are saved, since only a single field is used for slightly increased due to the incorporation of additional hardware
The number of machine cycles is reduced to the 50% of the initial configuration
The energy consumption is reduced by a factor of 2.5

---
Version 3: Effect of replacing chainable operations by single instructions (explanation)
Version 3: Effect of replacing chainable operations by single instructions (explanation)
Pattern matching for the MOV-SHL couple
MOVI R13, 0
SHL R13, R13, 8
MVISL R13, 0, 8
Assembly code for version 3 of the ASIP
Baseline assembly code
Micro-operation description for the MVISL operation
Instruction format: MVISL Rd, #immed, #shamt
Action: Rd  immed << shamt
shamt: shift amount (an immediate 5-bit value)

---
Version 3: Effect of replacing chainable operations by single instructions (expl. cont.)
Version 3: Effect of replacing chainable operations by single instructions (expl. cont.)
Pattern matching for the ADD-CMP-BLT triple
ADDI	Rix3, Rix3, 1
CMP	Rix3, Rfin3
BLT	loop3
FOR Rix3, #loop3
Assembly code for version 3 of the ASIP
Baseline assembly code
FOR instruction:
Instruction format: FOR Rd, #target_addr (I-format with Rs field unused)
Actions: Rd  Rd + Rstp ; flags: Rd - Rfin ; if (flags): PC  target_addr
“;” denotes concurrency in terms of control steps

---
Comparison
Comparison